## Slide 1: Sampling chip 3
Jean-Francois Genat, Herve Grabas, Eric Oberla
August 2d 2010

## Slide 2: Context
This chip aims to read Micro-Channel Plate devices coupled to
Transmission lines to provide large dimensions detectors with :
- 2-dimension readout with a 1mm precision (Dt=10ps)
- Time of flight timing 1-10ps

## Slide 3: Sampling electronics
Fast sampling electronics
- Records all the information from the detector pulse
- Provide picosecond timing resolution
See - G. Varner
- S. Ritt
- D. Breton, E. Delagnes

## Slide 4: Timing resolution
Differential timing resolution from T-line readout (10um MCP tube, 160PEs) for:
2-10GS/s sampling rates,
1 GHz 3dB analog bandwidth,
- 4-10 bit ADC resolutions.
No need to go much beyond 10GS/s and 7 bit with present MCPs.
Data taken at Argonne
(Ed May’s laser test stand)

## Slide 5: Guidelines
Push the 3dB analog bandwidth up to 1 GHz
Sampling rate up to 10-15GS/s
Digitize on-chip to 8-bit (and later signal process)
Use the130n same 130nm CMOS process

## Slide 6: Block-diagram