4-channel sampling chip design

Overview,  Architecture.

Use a switched capacitor array (SCA) as an analog memory clocked with a fast timing generator to record the history from a detector output.

First chip is a demonstrator: the goal is to obtain a timing resolution of a few picoseconds from fast MCP detectors after pulse reconstruction.

Design options:

15 GS/s sampling

1.5 GHz analog bandwidth

128 cells   (5-10ns recording time)

No PLL (to be implemented later)

4-channel

12-bit ADC

130nm CMOS technology

Pad Name	Type	Signal		Function

In_1-4		a I			Analog inputs    0 -1.2V

Trig      	a I			Trigger               0 -1.2V     Stops the recording process

MCk_n           d I       	diff		Write clock  (80 MHz to timing generator)

MCk_p

Ck_cv_n   	dO	diff		ADC clock output  (2 GHz/4096=500 kHz)

Ck_cv_p

Ck_rd_n   	d I        diff                  Read clock (50 MHz)

Ck_rd_p

VCN               aI                                 Controls delay of timing cell (falling)

VCP                aI                                                                                (rising)

V2GN             aI			Controls 2G counter ring oscillator

V2GP              aI

Ramp_n	a IO 	diff		External ramp input, or internal ramp output

Ramp_p

Mode_0-1	d I			00 write        writes continuously samples of inputs in a caps arrays at 15 GS/s

for 6.4us. Sampling stopped upon trigger

01 convert    starts ramp and counters at 2 GHz for 2 us

10 read         sequences 128 counters outputs onto data bus at 50 MHz

11 stand-by  clear sampling caps, reset counters

AD0-1					Channel address selects channel for read

D0-11		d I	3_state bus      12-bit data bus

Vdd					+1.2V

Vss                                                      - 1.2V

Gnd

Gnd   Gnd  In_1   Gnd  Vss  Vdd  Gnd  In_2  Gnd  Vss  Vdd Gnd  In_3 Gnd Vss  Vdd  Gnd   In_4  Gnd    Gnd

Vdd													   	   Vdd

VCN											                	               AD_0

VCP												  	    	   AD_1

Vss                                                                                                                                                                     Vss

Trig														   Gnd

Gnd													    	   D0

MCk_n	 									    	  	               D1

MCk_p												   	   D2

Gnd 													    	   D3

Ramp_p												               Vdd

Ramp_n                                                                                                                                                             Gnd

Ck_rd_n													   Gnd

Ck_rd_p                                                                                                                                                             Ck_cv_n

Gnd												         	               Ck_cv_p

Vss													               Gnd

Mode_0											           	               D4

Mode_1													   D5

Gnd   Vdd    Vss    Vdd    Gnd    Ck_rd_n  Ck_rd_p  Vss  Gnd D11   D10   Vdd   Gnd  D9   D8   D7   D6    Gnd

72 pads

# Text boxes

Ck_rd

128 cells

Timing generator

15 GS/s

Sampling Array (1 ch)

Data out

Data out

Ck_cv

Inputs 0-3

Control

Ramp

Delays

controls

Mode

MCk

Address