CDF Note 6998

Version 0.01

June 29, 2004

# Run IIB TDC-II Address Space

Mircea Bogdan and Harold Sanders

The University of Chicago

- Introduction

This note specifies the VME Address locations for the registers and RAMs on the TDC-II board [1] as well as the format for the Hit-Count and Hit-Data words.

- General VME Address Map

The VME Address Map for the TDC-II module is presented in Table 1. Each chip has its own set of control registers, ID Prom, Hit-data read-out buffer, Hit-count read-out buffer, Test_data RAM, XFT-freeze read-out RAM and XFR-DAQ read-out RAM. The first word in the ID Prom is the program version, the second one is the date. To write memory, the chips have to be in Test Mode (See Table 5, Register F).

Table 1. General VME address map.  Addr[31..27]=GA[4..0]; Addr[26..24] =0; Addr[1, 0] = 0.

| Name | Local VME Addr[23..2] | VME Addr[31..0] | VME Access | Number of words |
| --- | --- | --- | --- | --- |
| Control reg. - Chip0 | 0x000000 : 0x00000F | 0xYY000000 : 0xYY00003C | R/W | Table 2. |
| Control reg. - Chip1 | 0x004000 : 0x00400F | 0xYY010000 : 0xYY01003C | R/W | “ |
| Control reg. – VME Chip | 0x008000 : 0x00800F | 0xYY020000 : 0xYY02003C | R/W | Table 3. |
| ID Prom – Chip0 | 0x040000 : 0x04000F | 0xYY100000 : 0xYY10003C | R/O | 16 |
| ID Prom – Chip1 | 0x044000 : 0x04400F | 0xYY110000 : 0xYY11003C | R/O | 16 |
| Hit_data_buffer – Chip0 | 0x200000 : 0x20005F | 0xYY800000 : 0xYY80017C | R/W | Max 96 |
| Hit_data_buffer – Chip1 | 0x204000 : 0x20405F | 0xYY810000 : 0xYY81017C | R/W | “ |
| Hit_count_buffer – Chip0 | 0x240000 : 0x240005 | 0xYY900000 : 0xYY900014 | R/W | 7 |
| Hit_count_buffer – Chip1 | 0x244000 : 0x244005 | 0xYY910000 : 0xYY910014 | R/W | 7 |
| Test_data RAM – Chip0 | 0x1C0000 : 0x1C1FFF | 0xYY700000 : 0xYY707FFC | R/W | 8192 |
| Test_data RAM – Chip1 | 0x1C4000 : 0x1C5FFF | 0xYY710000 : 0xYY717FFC | R/W | 8192 |
| XFT_OutRAM – Chip0 | 0x280000 : 0x281FFF | 0xYYA00000 : 0xYYA07FFC | R/O | 8192 |
| XFT_OutRAM – Chip1 | 0x284000 : 0x285FFF | 0xYYA10000 : 0xYYA17FFC | R/O | 8192 |
| XFT_DAQ_RAM – Chip0 | 0x2C0000 : 0x2C003F | 0xYYB00000 : 0xYYB000FC | R/O | 128 |
| XFT_DAQ_RAM. – Chip1 | 0x2C4000 : 0x2C403F | 0xYYB10000 : 0xYYB100FC | R/O | 128 |
| Pulse Gen RAM – Chip0 (*) | 0x300000 : 0x3001FF | 0xYYC00000 : 0xYYC007FC | R/W | 512 |
| Pulse Gen RAM – Chip1(*) | 0x304000 : 0x3041FF | 0xYYC10000 : 0xYYC107FC | R/W | 512 |

(*) – Not available on TDC-II Prototype

- Data Format

After L2A, the XFT-DAQ-Readout buffer receives XFT_Lv2_length[5..0] words, the Hit Data Buffer in each chip receives 0 to 96 VME32 words and   the Hit Count Buffer in each chip receives seven VME32 words.

- XFT-DAQ-Readout Buffer  and XFT-Out RAM format

The format of the XTF-DAQ-Readout buffer in each of the two Stratix chips on board is presented in Table 2.

Table 2. XFT Readout Buffer and XFT-Out RAM

| XFT-DAQ/XFT-Out RAM Word [31..0] - Format |
| --- |
| 31..18 | 17 | 16 | 15..0 |
| 0x0 | XFT-Out B0 | XFT-Out Word 0 | XFT-Out_flags[15..0] |

- Hit Data Buffer format

The format of the VME words in the Hit-Data buffer in each of the two Stratix chips on board is presented in Table 3.

Table 3. Hit-Data Word

| Hit Data Word [31..0] - Format |
| --- |
| 31..24 | 23..16 | 15..8 | 7..0 |
| Leading Edge[7..0] | Width[7..0] | Leading Edge[7..0] | Width[7..0] |
| Channel m, Hit1 0 < m < 47 | Next Hit on same channel OR First hit on higher channel |
| ……………………………………………………. |
| Channel n, Hit j 0 < n < 47, 1 < j < 4 |  |
| ……………………………………………………. |

- Hit Count Buffer format

The format of the VME words in the Hit-Count buffer in each of the two Stratix chips on board is presented in Table 4.

The first word is a Header Word [2]:

Bit	7..0	Bunch ID: 8 bit counter from Bunch Zero;

12..8	Board Geographical Address;

22..13	Chip Serial Number – Set by a 10-bit DIP switch for each of the two STRATIX chips;

31..23	Chip Type

Six Hit Count VME32 Words, fallow the Header Word:

Bit	3	Channel ON/OFF Status

2..0	Actual Hit Count Value: between zero and four.

Table 4. Hit-Count Word

| Hit Count Word [31..0] - Format |
| --- |
| 31..28 | 27..24 | 23..20 | 19..16 | 15..12 | 11..8 | 7..4 | 3..0 |
| Hit Count Channel 7 | ……………………………………………. | Hit Count Channel 1 | Hit Count Channel 0 |
| ……………………………………………………………………. |
| Hit Count Channel 47 | ……………………………………………. | Hit Count Channel 41 | Hit Count Channel 40 |

- Pulse generator RAM Data format

Each TDC Chip has one LVDS transmitter. The output is synchronous with and repeats after each CDF_B0 pulse. Table 5 presents the format of the RAM holding the pattern for the LVDS transmitter.

Table 5. Pulse generator RAM word format

| Pulse Generator RAM Word [31..0] - Format |
| --- |
| 31..10 | 9..0 |
| 0x0 | RAM Word[9..0] |

- Control Registers

The locations of the control registers are presented in Table 5. These are words that map bits of the VME 32-bit data bus. Some words don’t use all 32 bits; the rest can be used as spare bits. To write a control register, the chips have to be in T/M (See Register F).  Exception: Register7 can be written any time but it’s effective only in VME_L2a mode.

Table 6. Control registers. Addr[31..27]=GA[4..0]; Addr[26..24] =0; Addr[1, 0] = 0.

| Register [bit] | Name | Access | Local VME Addr[23..2] | VME Addr[31..0] | Description |
| --- | --- | --- | --- | --- | --- |
| 0-0[31..8] 0-0[0] 0-0[1] 0-0[2] 0-0[3] 0-0[4] 0-0[7..5] | DEADBE Status-Chip0 “ “ “ “ “ | RO | 0x000000 “ “ “ “ “ “ | 0xYY000000 “ “ “ “ “ “ | Chip0,1-Program name Chip0- ID = 0. Chip0-Test_data vs. Real data mode Chip0-Test vs. Operation mode Chip0- XFT flavor Chip0-L2a from VME vs. DAQ 0x0 |
| 0-1[31..8] 0-1[0] 0-1[1] 0-1[2] 0-1[3] 0-1[4] 0-1[7..5] | DEADBE Status-Chip1 “ “ ““ “ “ | RO | 0x000000 “ “ “ “ | 0xYY010000 “ “ “ “ | Chip0,1-Program name Chip1- ID = 1. Chip1-Test_data vs. Real data mode Chip1-Test vs. Operation mode Chip1- XFT flavor Chip1-L2a from VME vs. DAQ 0x0 |
| 1-0[23..0] | WireMask0[23..0] | R/W | 0x000001 | 0xYY000004 | Chip0-Each L bit blocks corresponding wire |
| 1-1[23..0] | WireMask1[23..0] | R/W | 0x004001 | 0xYY010004 | Chip1-Each L bit blocks corresponding wire |
| 2-0[23..0] | WireMask0[47..24] | R/W | 0x000002 | 0xYY000008 | Chip0-Each L bit blocks corresponding wire |
| 2-1[23..0] | WireMask1[47..24] | R/W | 0x004002 | 0xYY010008 | Chip1-Each L bit blocks corresponding wire |
| 3-0[8..0] 3-0[21..16] | Pipe_size0[8..0] Lv2_length0[5..0] | R/W R/W | 0x000003 “ | 0xYY00000C “ | Chip0-Pipeline delay = 12ns x Pipe_size[] Chip0-L2 Buffer length = 12ns x Lv2_length[] |
| 3-1[8..0] 3-1[21..16] | Pipe_size1[8..0] Lv2_length1[5..0] | R/W R/W | 0x004003 “ | 0xYY01000C “ | Chip1-Pipeline delay = 12ns x Pipe_size[] Chip1-L2 Buffer length = 12ns x Lv2_length[] |
| 4-0[5..0] 4-0[11..6] 4-0[17..12] 4-0[23..18] | Brange0_0[5..0] Brange0_1[5..0] Brange0_2[5..0] Brange0_3[5..0] | R/W R/W R/W R/W | 0x000004 “ “ “ | 0xYY000010 “ “ “ | Chip0-Start of XFT Bin 0 Chip0-End of XFT BIN 0/Start of XFT Bin 1 Chip0-End of XFT BIN 1/Start of XFT Bin 2 Chip0-End of XFT BIN 2/Start of XFT Bin 3 |
| 4-1[5..0] 4-1[11..6] 4-1[17..12] 4-1[23..18] | Brange1_0[5..0] Brange1_1[5..0] Brange1_2[5..0] Brange1_3[5..0] | R/W R/W R/W R/W | 0x004004 “ “ “ | 0xYY010010 “ “ “ | Chip1-Start of XFT Bin 0 Chip1-End of XFT BIN 0/Start of XFT Bin 1 Chip1-End of XFT BIN 1/Start of XFT Bin 2 Chip1-End of XFT BIN 2/Start of XFT Bin 3 |
| 5-0[5..0] 5-0[11..6] 5-0[17..12] | Brange0_4[5..0] Brange0_5[5..0] Brange0_6[5..0] | R/W R/W R/W | 0x000005 “ “ | 0xYY000014 “ “ | Chip0-End of XFT BIN 3/Start of XFT Bin 4 Chip0-End of XFT BIN 4/Start of XFT Bin 5 Chip0-End of all XFT BINS |
| 5-1[5..0] 5-1[11..6] 5-1[17..12] | Brange1_4[5..0] Brange1_5[5..0] Brange1_6[5..0] | R/W R/W R/W | 0x004005 “ “ | 0xYY010014 “ “ | Chip1-End of XFT BIN 3/Start of XFT Bin 4 Chip1-End of XFT BIN 4/Start of XFT Bin 5 Chip1-End of all XFT BINS |
| 6-0[8..0] 6-0[21..16] | XPipe_size0[8..0] XLv2_length0[5..0] | R/W “ | 0x000006 “ | 0xYY000018 “ | Chip0-XFT_Pipeline delay=22ns x XPipe_size[] Chip0-XFT_L2 Buffer length = 22ns x XLv2_length[] |
| 6-1[8..0] 6-1[21..16] | XPipe_size1[8..0] XLv2_length1[5..0] | R/W “ | 0x004006 “ | 0xYY010018 “ | Chip1-XFT_Pipeline delay = 22ns x XPipe_size[] Chip1-XFT_L2 Buffer length = 22ns x XLv2_length[] |
| 7[1..0] | VME-cdfl2db0[1..0] | WO | 0x000007 | 0xYY00001C | VME Level2 Accept, where 7[1..0] = CDF_l2db[1..0]. |
| 8-0[7..0] | CDF_clk Del0 | R/W | 0x000008 | 0xYY000020 | Delay CTRL for CDF clock in 0.25ns steps – Chip0 |
| 8-0[15..8] | Bunch ID offset0 | R/W | “ | “ | Bunch ID offset – Chip0 |
| 8-1[7..0] | CDF_clk Del1 | R/W | 0x004008 | 0xYY010020 | Delay CTRL for CDF clock in 0.25ns steps – Chip1 |
| 8-1[15..8] | Bunch ID offset1 | R/W | “ | “ | Bunch ID offset – Chip1 |
| A-0[3..0] | DAQ Status Register | R/O | 0x00000A | 0xYY000028 | If a bit is ”1”, corresponding L2 Buffer has unprocessed data (“1” after L1A and “0” after L2A). – Chip0. |
| A-1[3..0] | DAQ Status Register | R/O | 0x00400A | 0xYY010028 | If a bit is ”1”, corresponding L2 Buffer has unprocessed data (“1” after L1A and “0” after L2A). – Chip1. |
| B[0] | VME_L2A Mode | WO | 0x00000B | 0xYY00002C | Put chips in VME_L2a mode by writing H”1” Put chips in DAQ_L2a mode by writing H”0” |
| C[0] | XFT flavor | WO | 0x00000C | 0xYY000030 | When H”0” – old style XFT When H”1” – new style XFT |
| D[0] | Test_data Mode | WO | 0x00000D | 0xYY000034 | When H”1” – Data is read from RAM instead of inputs When H”0” – Data is read from inputs |
| F[0] | Test Mode (T/M) | WO | 0x00000F | 0xYY00003C | Put chips in Test mode by writing H”1” Allows VME writes to chips; XFT_Out_RAM freeze. Put chips in Operation mode by writing H”0” |
| 11-0[] | Reset0 | WO | 0x000011 | 0xYY000044 | In T/M, a write at this address will clear registers – Chip0. |
| 11-1[] | Reset1 | WO | 0x000011 | 0xYY010044 | In T/M, a write at this address will clear registers – Chip1. |

- The VME Chip

The location of the control registers in the VME chip in presented in Table 6. To write the control register, the VME chip has to be in T/M.

Table 7. Cotrol Registers for the VME chip. Addr[31..27]=GA[4..0]; Addr[26..24] =0; Addr[1, 0] = 0.

| Register [bit] | Name | Access | Local VME Addr[23..2] | VME Addr[31..0] | Description |
| --- | --- | --- | --- | --- | --- |
| 0[15..4] 0[3..1] 0[1] 0[0] | XXXXBEE ZERO Status-VME Chip TDC_DONE | R/O | 0x008000 “ “ “ | 0xYY020000 “ “ “ | VME Chip – Program name 0x0 Test vs. Operation mode TDC_DONE bit |
| 1[0] 1[1] | CSR1- CBLTDIS CSR1-CBLTLAST | R/W R/W | 0x008001 “ | 0xYY020004 “ | When 1[0]=H”0”- CBLT enabled (default) When 1[0]=H”1”- CBLT disabled When 1[4]=H”0”- Not LAST Module in Chain (default) When 1[4]=H”1”- LAST Module in CBLT Chain |
| A[6..0] A[14..8] | Words0[6..0] Words1[6..0] | RO “ | 0x00800A “ | 0xYY020028 “ | Number of Hit Data words from Chip0 Number of Hit Data words from Chip1 |
| D[0] (*) | ECLpulse origin | R/W | 0x00800D | 0xYY020034 | When H”0” - Front Panel ECL pulses from backplane When H”1” - Front Panel ECL pulses from Chip0 |
| F[0] | VME Chip T/M | W/0 | 0x00800F | 0xYY02003C | Put VME Chip in T/M by writing H”1”. Put VME Chip on Operation Mode by writing H”0”. |
| 11[] (*) | Reconfigure | W/0 | 0x008011 | 0xYY020044 | In T/M, a write at this address will reconfigure both Stratix devices from the EPC16s. |

(*) – Not implemented in TDC-II Prototype.

- CBLT Function

The TDC module permits Chained Block Transfer (CBLT) read commands [3]. To disable CBLT and assign LAST module in the CBLT chain, set CSR1 according to Table5.  The same data is accessible for regular VME read-outs (See Table1).

There are two possible CBLT commands, as seen by the VME Crate CPU:

- Read block transfer from VME_Addr[31..27] = b”11111”(Slot 31). Hit_data  words are read from every CBLT enabled board in the crate (0 to 192 words/board).

- Read block transfer from VME_Addr[31..27] = b”11110”(Slot 30). Hit_count words are read from every CBLT enabled board in the crate (14 words/board).

- Reference

[1] M.Bogdan, et al, TDC-II Design and Specification: Run IIB TDC for the COT,

TDC Note 69989, 2004

[2]	T.Shaw and G. Sullivan, A Standard Front-End and Trigger VMEbus Based Readout

Crate for the CDF Upgrade – The CDF Readout Crate

CDF/DOC/TRIGGER/CDFR/2338, 1993.

[23] ANSI/VITA 23-1998, Approved March 22, 1998.